## Slide 1: Lecture for Storage System
Type of Storage Devices
Buses—Connecting I/O Devices to CPU/Memory
Reliability,Availability,and Dependability
RAID: Redundant Arrays of Inexpensive Disks
Error and Failures in Real Systems
I/O Performance Measures
A Little Queuing Theory
1

## Slide 2: 7.1 Introduction
The prejudice
  Historically neglected by CPU enthusiasts
    CPU time which by definition ignores I/O
  Citizenship of I/O is even apparent in the label peripheral applied to I/O devices.
The fact
  A computer without I/O devices is like a car without wheels
    You can’t get very far without them.
  response time
    The time between when the user types a command and when results appear—is surely a better measure of performance.
2

## Slide 3: Does I/O Performance Matter?
One argument : I/O speed doesn’t matter
  If a process waits for a peripheral, run another task
  Throughput does not descend
  I/O performance doesn’t matter in a multiprogrammed environment.
Several points to make in reply
  if users didn’t care about response time
    Interactive software never would have been invented
    Be no workstations or personal computers today;
  Expensive to rely on running other processes
    Paging traffic from process switching might actually increase I/O.
    Mobile devices and desktop computing, there is only one person per computer and thus fewer processes than in timesharing.
  Many times the only waiting process is the human being!
3

## Slide 4: I/O’s Revenge is at hand
Amdahl's Law: system speed-up limited by the slowest part!
  10% IO & 10x CPU => (lose 50%)
  10% IO & 100x CPU => (lose 90%)
I/O bottleneck:
    Diminishing fraction of time in CPU
    Diminishing value of faster CPUs
I/O performance increasingly limits system performance and effectiveness
  CPU Performance: 55% per year and I/O did not improve
  Every task would become I/O bound.
  There would be no reason to buy faster CPUs—and no jobs for CPU designers.
Speedup=
1
0.1+0.09
=5
Speedup=
1
0.1+0.009
=10
Notes: Ancestor of Java had no I/O
CPU vs. Peripheral
Primary vs. Secondary
What maks portable, PDA exciting?

## Slide 5: Does CPU Performance Matter?
Why still important to keep CPUs busy vs. IO devices ("CPU time"), as CPUs not costly?
  Moore's Law leads to both large, fast CPUs but also to very small, cheap CPUs
  2001 Hypothesis: 600 MHz PC is fast enough for Office Tools?
  PC slowdown since fast enough unless games, new apps?
People care more about storing information and communicating information than calculating
  "Information Technology" vs. "Computer Science"
  1960s and 1980s: Computing Revolution
  1990s and 2000s: Information Age
This shift in focus from computation to communication and storage of information
  emphasizes reliability, availability and scalability as well as cost-performance.

## Slide 6: Types of Storage Devices-1
Device Providing Information
Sensor Key CRT
1~1000B/S 10B/S 2000B/S
  Printer Communication Cable
1800B/S 30~200000B/S
Multimedia Data Device
    high speed graphics video display Audio frequency
1MB/S 100MB/S 64KB/S
Network Communication
DIX ( Ethernet network standard Digital, Intel, Xerox)、TB2、RJ45

## Slide 7: Types of Storage Devices-2
Device Behavior Partner Data Rate (KB/sec)
Keyboard Input Human 0.01
Mouse Input Human 0.02
Printer Output Human 3.00
Floppy disk Storage Machine 50.00
Laser Printer Output Human 100.00
Optical Disk Storage Machine 500.00
Magnetic Disk Storage Machine 5,000.00
Network-LAN Input or Output Machine 20 --1,000.00
Graphics Display Output Human 30,000.00

## Slide 8: Storage Technology Drivers
Driven by the prevailing computing paradigm
  1950s: migration from batch to on-line processing
  1990s: migration to ubiquitous computing
    computers in phones, books, cars, video cameras, …
    nationwide fiber optical network with wireless tails
Effects on storage industry:
  Embedded storage
    smaller, cheaper, more reliable, lower power
  Data utilities
    high capacity, hierarchically managed storage

## Slide 9: I/O Systems
Processor
Cache
Memory - I/O Bus
Main
Memory
I/O
Controller
Disk
Disk
I/O
Controller
I/O
Controller
Graphics
Network
interrupts

## Slide 10: Disk Device Terminology
Several platters, with information recorded magnetically on both surfaces (usually)
Platter
Outer
Track
Inner
Track
Sector
Actuator
Head
Arm

## Slide 11: Disk Device Terminology
Actuator moves head (end of arm,1/surface) over track (“seek”), select surface, wait for sector rotate under head, then read or write “Cylinder”: all tracks under heads
Bits recorded in tracks, which in turn divided into sectors (e.g., 512 Bytes)

## Slide 12: What’s Inside A Disk Drive?

## Slide 13: Disk Device Performance
Seek time: move head to the desired track
  today’s drives - 5 to 15 ms
  average seek = time for all possible seeks/no. of possible seeks
  actual average seek = 25% to 33% due to locality
Rotational latency
  today’s drives - 5,400 to 12,000 RPM ;
  approximately 12 ms to 5 ms
  average rotational latency = (0.5)(rotational latency)
Transfer time
  time to transfer a sector (1 KB/sector)
  function of rotation speed, recording density
  today’s drives - 10 to 40 MBytes/second
Controller time
  overhead on drive electronics adds to manage drive
  but also gives prefetching and caching
Disk Latency = Seek Time + Rotation Time + Transfer Time + Controller Overhead

## Slide 14: Disk Device Performance-2 Average access time = (seek time) + (rotational latency) + (transfer) + (controller time)
Track and cylinder skew
  cylinder switch time
    delay to change from one cylinder to the next
      may have to wait an extra rotation
    solution - drives incorporate skew
      offset sectors between cylinders to account for switch time
  head switch time
    change heads to go from one track to next on same cylinder
      incur additional settling time
Prefetching
  disks usually read an entire track at a time
  assumes that request for the next sector will come soon
Caching
  limited amount of caching across requests, but prefetching is preferred

## Slide 15: Disk Device Performance-3
Average distance sector from head?
1/2 time of a rotation
  10000 Revolutions Per Minute  166.67 Rev/sec
  1 revolution = 1/ 166.67 sec  6.00 milliseconds
  1/2 rotation (revolution)  3.00 ms
Average no. tracks move arm?
  Sum all possible seek distances from all possible tracks / # possible
    Assumes average seek distance is random
  Disk industry standard benchmark

## Slide 16: Data Rate: Inner vs. Outer Tracks
To keep things simple, originally kept same number of sectors per track
  Since outer track longer, lower bits per inch
Competition decided to keep BPI the same for all tracks (“constant bit density”)
  More capacity per disk
  More of sectors per track towards edge
  Since disk spins at constant speed, outer tracks have faster data rate
Bandwidth outer track 1.7X inner track!
  Inner track highest density, outer track lowest, so not really constant
  2.1X length of track outer / inner, 1.7X bits outer / inner

## Slide 17: Devices: Magnetic Disks
Purpose:
  Long-term, nonvolatile storage
  Large, inexpensive, slow level in the storage hierarchy
Characteristics:
  Seek Time (~8 ms avg)
    positional latency
    rotational latency
  Transfer rate
    10-40 MByte/sec
    Blocks
  Capacity
    Gigabytes
    Quadruples every 2 years (aerodynamics)
Response time
= Queue + Controller + Seek + Rot + Xfer
Service time

## Slide 18: State of the Art: Barracuda 180
  181.6 GB, 3.5 inch disk
  12 platters, 24 surfaces
  24,247 cylinders
  7,200 RPM; (4.2 ms avg. latency)
  7.4/8.2 ms avg. seek (r/w)
  64 to 35 MB/s (internal)
  0.1 ms controller time
  10.3 watts (idle)
source: www.seagate.com
Latency =
Queuing Time +
Controller time +
Seek Time + Rotation Time +
Size / Bandwidth
per access
per byte
{
+
Sector
Track
Cylinder
Head
Platter
Arm
Track Buffer
Notes: 47 to 26 MB/s (external)

## Slide 19: Disk Performance Example
Disk characteristics
  512 byte sector, rotate at 5400 RPM, advertised seeks is 5 ms,
  transfer rate is 40 MB/sec, it rotates at 10,000RPM, controller overhead is 0.1 ms, queue idle so no service time.
Answer
  Access Time = Seek time + Rotational Latency + Transfer time + Controller Time + Queuing Delay
＝5ms ＋
0.5
10,000PRM
＋
0.5KB
40MB/sec
＋ 0.1ms
＝5ms ＋ 3.0 ＋ 0.013 ＋ 0.1 ＝8.11ms

## Slide 20: Disk Performance Example(cont.)
Access Time ＝33%×5ms ＋ 3.0 ms＋ 0.013ms ＋ 0.1ms ＝4.783ms
Assuming the measured seek time is 33% of the calculated average, the answer is
Note that only 0.013 /4.783 or 0.3% of the time is the disk transferring data in this example. Even page-sized transfers often take less than 5%, so disks normally spend most of their time waiting for the head to get over the data rather than reading or writing the data.

## Slide 21: The Future of Magnetic Disks
Bits recorded along a track
  Metric is Bits Per Inch (BPI)
Number of tracks per surface
  Metric is Tracks Per Inch (TPI)
Disk Designs Brag about bit density per unit area
  Metric is Bits Per Square Inch
  Called Areal Density
  Areal Density = BPI x TPI

## Slide 22: Areal Density
  Areal Density = BPI x TPI
  Change slope 29%/yr to 60%/yr about 1996

## Slide 23: 1 inch disk drive!
2000 IBM MicroDrive:
  1.7” x 1.4” x 0.2”
  1 GB, 3600 RPM, 5 MB/s, 15 ms seek
  Digital camera, PalmPC?
2006 MicroDrive?
9 GB, 50 MB/s!
  Assuming it finds a niche in a successful product
  Assuming past trends continue

## Slide 24: Optical Disks
One challenger
  High capacity、Low cost
  Read-onlyWrite onceReWritable
  CD-DA、CD-ROM、CD-I、CD-R、VCD、DVD
  Pits(0.5μm)、lands、

## Slide 25: Magnetic Tapes vs. Disk
Longitudinal tape uses same technology as hard disk; tracks its density improvements
Disk head flies above surface, tape head lies on surface
Disk fixed, tape removable
Inherent cost-performance based on geometries:
fixed rotating platters with gaps
  (random access, limited area, 1 media / reader)
removable long strips wound on spool
  (sequential access, "unlimited" length, multiple / reader)
Helical Scan (VCR, Camcoder, DAT)
  Spins head at angle to tape to improve density

## Slide 26: Current Drawbacks to Tape
Tape wear out:
  Helical 100s of passes to 1000s for longitudinal
Head wear out:
  2000 hours for helical
Both must be accounted for in economic / reliability model
Bits stretch
Readers must be compatible with multiple generations of media
Long rewind, eject, load, spin-up times; not inherent, just no need in marketplace
Designed for archival

## Slide 27: Automated Tape Libraries StorageTek Powderhorn 9310
6000 x 50 GB 9830 tapes = 300 TBytes in 2000 (uncompressed)
  Library of Congress: all information in the world; in 1992, ASCII of all books = 30 TB
  Exchange up to 450 tapes per hour (8 secs/tape)
1.7 to 7.7 Mbyte/sec per reader, up to 10 readers
7.7 feet
10.7 feet
8200 pounds, 1.1 kilowatts

## Slide 28: Library vs. Storage
Getting books today as quaint as the way I learned to program
  punch cards, batch processing
  wander thru shelves, anticipatory purchasing
Cost $1 per book to check out
$30 for a catalogue entry
30% of all books never checked out
Write only journals?
Digital library can transform campuses

## Slide 29: Whither tape?
Investment in research:
  90% of disks shipped in PCs; 100% of PCs have disks
  ~0% of tape readers shipped in PCs; ~0% of PCs have disks
Before, N disks / tape; today, N tapes / disk
  40 GB/DLT tape (uncompressed)
  80 to 192 GB/3.5" disk (uncompressed)
Cost per GB:
  In past, 10X to 100X tape cartridge vs. disk
  Jan 2001: 40 GB for $53 (DLT cartridge), $2800 for reader
  $1.33/GB cartridge, $2.03/GB 100 cartridges + 1 reader
  ($10995 for 1 reader + 15 tape autoloader, $10.50/GB)
  Jan 2001: 80 GB for $244 (IDE,5400 RPM), $3.05/GB
  Will $/GB tape v. disk cross in 2001? 2002? 2003?
Storage field is based on tape backup; what should we do? Discussion if time permits?

## Slide 30: What about FLASH
Compact Flash Cards
  Intel Strata Flash
    16 Mb in 1 square cm. (.6 mm thick)
  100,000 write/erase cycles.
  Standby current = 100uA, write = 45mA
  Compact Flash 256MB~=$120 512MB~=$542
  Transfer @ 3.5MB/s
IBM Microdrive 1G~370
  Standby current = 20mA, write = 250mA
  Efficiency advertised in wats/MB
Disks
  Nearly instant standby wake-up time
  Random access to data stored
  Tolerant to shock and vibration (1000G of operating shock)

## Slide 31: 7.3 Buses--Connecting I/O Devices to CPU/Memory
Lots of sub-systems need to communicate
Busses: Shared wires for common communication

## Slide 32: Bus Classifications
CPU-memory busses
  Fast
  Proprietary
  Closed and controlled
  Support only memory transactions
IO busses
  Standardized (SCSI, PCI, AGP)
  More diversity
  More length
Bus Bridges/Adapter
  Standardized (RS-232, )
  Cross from one bus to another

## Slide 33: Bus Design Decisions
goals
  decisions depend on cost and performance
  higher performance at more cost.
The first three options in the figure are clear
  separate address and data lines,
  wider data lines, and multiple
  word transfers

## Slide 34: Structure, Width, and Transfer Length
Separate vs. Multiplexed Address/Data
  Multiplexed: save wires
  Separate: more performance
Wide words: higher throughput, less control per transfer
  On-chip cache to CPU busses: 256 bits wide
  Serial Busses
Data Transfer Length
  More data per address/control transfer
Example: Multiplexed Addr/Data with Data transfer of 4

## Slide 35: Bus Mastering
Bus Master: a device that can initiate a bus transfer
    1. CPU makes memory request
    2. Page Fault in VM requires disk access to load page
    3. Mover data from disk to memory
If the CPU is master, does it have to check to see if the disk is ready to transfer?

## Slide 36: Multiple Bus Masters
What if multiple devices could initiate transfers?
  Update might take place in background while CPU operates
Multiple CPUs on shared memory systems
Challenge: Arbitration
  If two or more masters want the bus at the same time, who gets it?

## Slide 37: Bus Clocking: Synchronous
Synchronous
  Sample the control signals at edge of clock
Pro: Fast and High Performance
Con:
  Can’t be long (skew) or fast at same time
  All bus members must run at the right speed

## Slide 38: Bus Clocking: Asynchronous
Asynchronous
  Edge of control signals determines communication
  “Handshake Protocol”
Pros:
  No clock
  Slow and fast components on the same bus
Con:
  Inefficient: two round trips
  Like somebody who always repeats what was said to them
1. Request (with actual transaction)
2. Acknowledge causes de-assert of Request
3. De-assert of Request causes de-assert of Ack
4. De-assert of Ack allows re-assertion of Request

## Slide 39: Synchronous vs Asynchronous
Preferred bus type as a function of length/clock skew and variation in I/O device speed.
Synchronous is best when the distance is short and the I/O devices on the bus all transfer at similar speeds.

## Slide 40: Split Transactions
Problem: Long wait times
Solution: Split Transaction Bus

## Slide 41: Bus Standards
I/O bus --- interface---devices
Standards
  let the computer designer and I/O-device designer work independently play a large role in buses.
  Any I/O device can connect to any computer.
Document
  Defines how to connect devices to computers
De facto standards
  Machines sometimes grow to be so popular that their I/O buses become de facto standards
  PDP-11 Unibus、IBM PC-AT

## Slide 42: Examples of Buses
Buses in common use
  Common desktop I/O buses,
  I/O buses found in embedded devices,
  CPU-memory interconnects found in servers
Summary of parallel I/O buses.
Summary of serial I/O buses ( Embedded computers)
Summary of CPU-memory interconnects found in 2000 servers.

## Slide 43: Summary of parallel I/O buses
IDE---Integrated Drive Electronics
  Early disk standard that connects two disks to a PC.
  It has been extended by AT-bus Attachment (ATA), to be both wider and faster.
SCSI---Small Computer System Interconnect
  connects up to 7 devices for 8-bit busses and up to 15 devices for 16-bit busses.
  They can even be different speeds, but they run at the rate of the slowest device.
  The peak bandwidth of a SCIS bus is the width (1 or 2 bytes) times the clock rate (10 to 160 MHz). Most SCSI buses today are 16-bits.
PCI---Peripheral Component Interconnect
PCI-X ,PCI Extended
  Connect main memory to peripheral devices

## Slide 44: Summary of parallel I/O buses

## Slide 45: Summary of serial I/O buses
Often used in embedded computers.
I2C ----- invented by Phillips in the early 1980s.
1-wire -- developed by Dallas Semiconductor.
RS-232 -introduced in 1962.
SPI ----- created by Motorola in the early 1980s.

## Slide 46: Summary of CPU-memory interconnects found in 2000 servers
Shared bus
crossbars switches
  Each bus connects up to four processors and memory controllers, and then the crossbar connects the busses together.
  The number of slots in the crossbar is 16, 8, and 16, respectively.
  These servers use crossbars switches to connect nodes processors together instead of a shared bus interconnect.

## Slide 47: 7.5 RAID: Redundant Arrays of Inexpensive Disks
A disk arrays replace larger disk

## Slide 48
David patterson, Garth Gibson, and Randy Katz, A Case for Redundant Arrays of Inexpensive Disks (RAID), ACM SIGMOD conference, 1988

## Slide 49: Use Arrays of Small Disks?
Low End
High End
3.5”
Disk Array: 1 disk design
14”
10”
5.25”
3.5”
Conventional: 4 disk designs
Katz and Patterson asked in 1987:
    Can smaller disks be used to close gap in performance between disks and CPUs?

## Slide 50: Replace Small Number of Large Disks with Large Number of Small Disks! (1988 Disks)
Capacity
Volume
Power
Data Rate
I/O Rate
MTTF
Cost
IBM 3390K
20 GBytes
97 cu. ft.
3 KW
15 MB/s
600 I/Os/s
250 KHrs
$250K
IBM 3.5" 0061
320 MBytes
0.1 cu. ft.
11 W
1.5 MB/s
55 I/Os/s
50 KHrs
$2K
x70
23 GBytes
11 cu. ft.
1 KW
120 MB/s
3900 IOs/s
??? Hrs
$150K
Disk Arrays have potential for large data and I/O rates, high MB per cu. ft., high MB per KW, but what about reliability?
9X
3X
8X
6X

## Slide 51: Array Reliability
Reliability of N disks = Reliability of 1 Disk ÷ N
  50,000 Hours ÷ 70 disks = 700 hours
Disk system MTTF: Drops from 6 years to 1 month!
• Arrays (without redundancy) too unreliable to be useful!
Hot spares support reconstruction in parallel with access: very high media availability can be achieved

## Slide 52: Redundant Arrays of (Inexpensive) Disks
Files are "striped" across multiple disks
Redundancy yields high data availability
  Availability: service still provided to user, even if some components failed
Disks will still fail
Contents reconstructed from data redundantly stored in the array
   Capacity penalty to store redundant info
   Bandwidth penalty to update redundant info

## Slide 53: RAID 0: No Redundancy
Data is striped across a disk array but there is no redundancy to tolerate disk failure
It also improves performance for large accesses, since many diskscan operate at once.
RAID 0 something of a misnomer as there is no redundancy,

## Slide 54: RAID 1: Disk Mirroring/Shadowing
• Each disk is fully duplicated onto its “mirror”
Very high availability can be achieved
• Bandwidth sacrifice on write:
Logical write = two physical writes
  • Reads may be optimized
• Most expensive solution: 100% capacity overhead
(RAID 2 not interesting, so skip)
recovery
group

## Slide 55: RAID 3: Bit-Interleaved Parity Disk
10010011
11001101
10010011
. . .
logical record
P contains sum of
other disks per stripe mod 2 (“parity”)
If disk fails, subtract
P from sum of other disks to find missing information
Striped physical
records
P
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1

## Slide 56: RAID 3
Sum computed across recovery group to protect against hard disk failures, stored in P disk
Logically, a single high capacity, high transfer rate disk: good for large transfers
Wider arrays reduce capacity costs, but decreases availability
33% capacity cost for parity in this configuration

## Slide 57: Inspiration for RAID 4
RAID 3 relies on parity disk to discover errors on Read
But every sector has an error detection field
Rely on error detection field to catch errors on read, not on the parity disk
Allows independent reads to different disks simultaneously

## Slide 58: RAID 4: High I/O Rate Parity
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Address
Stripe
Insides of 5 disks
Example:
small read D0 & D5, large write D12-D15

## Slide 59: Inspiration for RAID 5
RAID 4 works well for small reads
Small writes (write to one disk):
  Option 1: read other data disks, create new sum and write to Parity Disk
  Option 2: since P has old sum, compare old data to new data, add the difference to P
Small writes are limited by Parity Disk: Write to D0, D5 both also write to P disk
D0
D1
D2
D3
P
D4
D5
D6
P
D7

## Slide 60: RAID 5: High I/O Rate Interleaved Parity
Independent writes
possible because of
interleaved parity
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Addresses
Example: write to D0, D5 uses disks 0, 1, 3, 4

## Slide 61: Problems of Disk Arrays: Small Writes
D0
D1
D2
D3
P
D0'
+
+
D0'
D1
D2
D3
P'
new
data
old
data
old
parity
XOR
XOR
(1. Read)
(2. Read)
(3. Write)
(4. Write)
RAID-5: Small Write Algorithm
1 Logical Write = 2 Physical Reads + 2 Physical Writes

## Slide 62: RAID-DP: P365 in 4th Edition
Protect against double failure
  Row parity: one parity for per-stripe in red
  Diagonal parity: showed in blue.
  Row-Diagonal for p=5
    P-1 dada disk, 1 row parity, 1 diagonal parity, total P+1 disk
  -

## Slide 63: Case: Recovery of double failure
Recovery solution 1:
   D3-0(from Diagonal parity)
   D1-3( from Row parity)
   D3-3(Diagonal Parity)
   D1-1(Row parity )
   D2-2(Diagonal Parity)
   D3-4(Row Parity )
   D3-1 (Diagonal Parity)
   D1-4 (Row Parity)

## Slide 64: System Availability: Orthogonal RAIDs
Data Recovery Group: unit of data redundancy
Redundant Support Components: fans, power supplies, controller, cables
Array
Controller
String
Controller
String
Controller
String
Controller
String
Controller
String
Controller
String
Controller
. . .
. . .
. . .
. . .
. . .
. . .
End to End Data Integrity: internal parity protected data paths

## Slide 65: System-Level Availability
Fully dual redundant
I/O Controller
I/O Controller
Array Controller
Array Controller
. . .
. . .
. . .
. . .
. . .
.
.
.
Recovery
Group
Goal: No Single
Points of
Failure
host
host
with duplicated paths, higher performance can be
obtained when there are no failures

## Slide 66: Summary: RAID Techniques: Goal was performance, popularity due to reliability of storage
• Disk Mirroring, Shadowing (RAID 1)
Each disk is fully duplicated onto its "shadow"
Logical write = two physical writes
100% capacity overhead
• Parity Data Bandwidth Array (RAID 3)
Parity computed horizontally
Logically a single high data bw disk
• High I/O Rate Parity Array (RAID 5)
Interleaved parity blocks
Independent reads and writes
Logical write = 2 reads + 2 writes
1
0
0
1
0
0
1
1
1
1
0
0
1
1
0
1
1
0
0
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
0
1
0
0
1
1
1
0
0
1
0
0
1
1

## Slide 67: 7.7 I/O Performance Measures
I/O System performance depends on many aspects of the system (‘limited by weakest link in the chain’)
  The CPU
  The memory system:
    Internal and external caches
    Main Memory
  The underlying interconnection (buses)
  The I/O controller
  The I/O device
  The speed of the I/O software (Operating System)
  The efficiency of the software¡¯s use of the I/O devices
Two common performance metrics:
  Throughput: I/O bandwidth
  Response time: Latency

## Slide 68: Simple Producer-Server Model
Throughput
  The number of tasks completed by the server in unit time
  In order to get the highest possible throughput:
    The server should never be idle
    The queue should never be empty
Response time
  Begins when a task is placed in the queue
  Ends when it is completed by the server
  In order to minimize the response time:
    The queue should be empty
    The server will be idle

## Slide 69: Throughput versus Respond Time

## Slide 70: Response time relate to Interaction
An interaction, or transaction, with a computer is divided into three parts:
1. Entry time---The time for the user to enter the command.
  The graphics system required 0.25 seconds on average to enter a command versus 4.0 seconds for the keyboard system.
2. System response time---The time between when the user enters the command and the complete response is displayed.
3. Think time---The time from the reception of the response until the user begins to enter the next command.

## Slide 71: Response time relate to Interaction

## Slide 72: Response time vs Manipulator

## Slide 73: 7.8 A Little Queuing Theory
Assumption: steady state characteristics, FIFO
Little’s Law:
LengthSystem = Arrival rate x TimeSystem
(LengthQueue + LengthServer) = l x (TimeQueue + TimeServer)

## Slide 74: How busy a system is !
Server Utilization (U)
U = l x TimeServer
(Arrival Rate < Service Rate)
Example:
  Single disk (server) gets 10 requests per second
  Avg time to service a request: 50 ms
What is the utilization?
  Arrival rate: 10 IOPS
  Service rate: 1/50ms = 20 IOPS
  How many requests at the disk on average?
LengthServer = Arrival rate x TimeServer = 10 IOPS x 0.05s
= 0.5 in disk at any one time
Server Utilization = -------------------
Arrival rate
Service rate
Server Utilization = ------- =50%
10
20

## Slide 75
For I/O systems
(making some assumptions + doing a little algebra)
Tqueue = Tserver x U / (1-U)
Lqueue= U2 / (1-U)

## Slide 76: Throughput Enhancement-1
In general throughput can be improved by:
  Throwing more hardware at the problem
Parallel Queues
  Increases system throughput
Problem: One queue is full while other is empty

## Slide 77: Throughput Enhancement-2
Little’s Law still holds
Server utilization could be greater than 1.0
Response time is much harder to reduce
  Minimum: 1/Tserver