## Slide 1: Discussion: Meltdown & Spectre
陈文智
浙江大学计算机学院
chenwz@zju.edu.cn

## Slide 2: TOC
Introduction
  Optimization techniques in modern processors
  Cache
Security vulnerabilities
  Meltdown
  Spectre
Mitigations
  Software
  Hardware

## Slide 3: Optimization techniques in modern processors
Complicated optimization techniques are widely used in modern processors
  Out-of-order execution
    Processor executes instructions in an order governed by the availability of input data and units, rather than the original program.
    If an instruction causes an exception, out-of-order executed code after this instruction in original program should be reverted.
  Speculative execution
    Predict the execution path and do the tasks before it is known whether it is actually needed.
    Example: Branch prediction
    If it turns out the prediction is incorrect, changes made by speculative-executed code should be reverted.

## Slide 4: Cache
Cache fundamentally provide faster access to frequently used data
  Closer to execution core, less time for access
Difference in access time can be measured by software
  Cached data will take fewer cycles to access
  Measure access time precisely is possible on many architectures (e.g. RDTSC instruction on x86)
Thus, it is possible to determine whether a specific address is in the cache
  By comparing the access time with known cached/not cached data

## Slide 5: Meltdown & Spectre Overview
Meltdown
  out-of-order execution
  Relies on the design feature of processor’s MMU
    All Intel x86 CPUs are affected
    Some processors are not affected
Spectre
  speculative execution (mostly branch prediction)
  A more generalized idea
    Several attack variants discovered
  Does not rely on a specific processor feature
    Almost every modern PC/mobile processor is affected

## Slide 6: Meltdown
Memory privilege check bypass
  Allows an unauthorized process to read data from any memory address, even it have no permission
Exploits out-of-order execution
  An instruction reads privileged memory, which will cause an exception
  Out-of-order executed code after that should be reverted
    However, the cache load operation is not reverted
  An attacker could ‘convert’ the byte read from privileged memory to a cache load operation
    By accessing a memory address that was calculated from the byte read from privileged memory
    After exception, that byte can be recovered by finding which memory address was cached

## Slide 7: Spectre
Branch misprediction may leave observable side effects
  For example: cache status
Branch prediction units can be “trained” to reliable outputs
  Attacker can trick a program into a execution path that leak private data to cache status, then extract information from by cache
Several variants have been discovered

## Slide 8: Spectre Variant 1: Bounds Check Bypass
Sandbox/VMs are commonly used for running untrusted code
  For example, JavaScript in web browser
  Bound check ensures the code in VM can only access authorized memory regions
Bound check may be mis-predicted as success
  The code after bound check may executed speculatively even the bound check is not success
  Attacker can covert the out-of-bound data read to a cache load behavior, then extract data from cache state
Result: JavaScript in web browser can access private data without boundary limitations

## Slide 9: Spectre Variant 2: Branch Target Injection
Indirect branch predictor
  Indirect branch: branch target is not directly provided by instruction
    For example: jump to the address in r1 register
  Indirect branch predictor stores the history of branch target addresses, and use them to predict the target of next branch
Attack can “train” the result of indirect branch predictor
  Train the speculative execution path to attacker’s code
  Leak the private data to cache state

## Slide 10: More Variants
Vulnerability | CVE | Exploit name | Public vulnerability name
Spectre | 2017-5753 | Variant 1 | Bounds Check Bypass (BCB)
Spectre | 2017-5715 | Variant 2 | Branch Target Injection (BTI)
Spectre-NG | 2018-3640 | Variant 3a | Rogue System Register Read (RSRE)
Spectre-NG | 2018-3639 | Variant 4 | Speculative Store Bypass (SSB)
Spectre-NG | 2018-3665 |  | Lazy FP State Restore
Spectre-NG | 2018-3693 | Variant 1.1 | Bounds Check Bypass Store (BCBS)
Spectre |  | Variant 1.2 | Read-only protection bypass (RPB)
SpectreRSB |  |  | Return Mispredict

## Slide 11: Software Mitigations
Meltdown: Kernel page-table isolations(KPTI)
  Isolate the page table of kernel space and user space
    Make speculative read of kernel memory not possible
  Require TLB flush on every switch between kernel and user mode
    Heavy performance cost
Spectre
  Variant 1
    Modify software in order to prevent speculative load on bound checks
  Variant 2
    Retpoline (solution by Google)

## Slide 12: Hardware Mitigations
Meltdown
  Prevent out-of-order execution relies on the result of memory access before privilege check confirmed.
Spectre
  Disable branch predictor?
    Huge performance loss
  Isolate predictor state from different applications
  New instructions to restrict speculative execution behaviors

## Slide 13: Readings
Papers
  https://meltdownattack.com/meltdown.pdf
  https://spectreattack.com/spectre.pdf
New variants recently discovered
  Variant 4: https://blogs.technet.microsoft.com/srd/2018/05/21/analysis-and-mitigation-of-speculative-store-bypass-cve-2018-3639/
  NetSpectre: https://mlq.me/download/netspectre.pdf
  Foreshadow: https://www.usenix.org/system/files/conference/usenixsecurity18/sec18-van_bulck.pdf
Articles
  Analysis from Intel: https://newsroom.intel.com/wp-content/uploads/sites/11/2018/01/Intel-Analysis-of-Speculative-Execution-Side-Channels.pdf
  Retpoline: https://software.intel.com/security-software-guidance/api-app/sites/default/files/Retpoline-A-Branch-Target-Injection-Mitigation.pdf
Discussions
  http://research.cs.wisc.edu/multifacet/papers/hill_mark_wisconsin_meltdown_spectre.pdf
  https://people.redhat.com/jcm/talks/FOSDEM_2018.pdf