## Slide 1: Computer Architecture ----A Quantitative Approach
陈文智
浙江大学计算机学院
chenwz@zju.edu.cn

## Slide 2: Instruction Set Architecture

## Slide 3: Instruction Set Architecture

## Slide 4: Instruction Set Design Tasks
Classifying Instruction Set Architectures
Memory Addressing
Operations in the Instruction Set
Type and Size of Operands
Encoding an Instruction Set
Optimizing an Instruction Set

## Slide 5: 2.10 Encoding an Instruction Set
Encoding affect:
  Size of compiled program
  the implementation of the CPU
Balancing forces:
  From the compiler viewpoint: to have as many registers and addressing modes as possible
  Impact of register size and addressing mode fields on Average instruction size、average program size
  Easy to implement

## Slide 6: Key factors for Encoding
Key Factors
  The range of addressing modes
  The degree of independence between opcodes and addressing modes

## Slide 7: Three popular choices for instruction encoding
Operation &
Address
Address
no. of operands
specifier1
Address
Address
specifier n
field n
Operation &
Address
Address
Address
no. of operands
field 1 field 2 field 3
Operation
Address
specifier field
Operation
Address
Address
specifier1 specifier2 field
Operation
Address
Address
specifier field 1 field 2
…
(a)
Variable(e.g.,VAX,Intel 80x86)
(b)
Fixed(e.g.,Alpha,ARM,MIPS,PowerPC,SPARC,SuperH)
(c)
Hybrid(e.g.,IBM360/70,MIPS16,Thumb,TI TMS320C54x)
field 1
Address
Address
Address

## Slide 8: Comparison of three instruction encoding formats
Variable length：
  Number of operations and addressing modes is big
  Small program size, high code density, a variety of formats for one instruction
Fixed length：
  Number of operations and addressing modes is small
  Large program size, low code density, fixed format, easy to implement
Hybrid
  Has multiple formats specified by the opcode, adding or or two fields to specify the addressing mode and one or two fields to specify the operand address

## Slide 9: Reduced Code Size in RISCs
New hybrid version of RISC instructions, with both 16-bit and 32-bit instructions.
  ARM Thumb , MIPS16
IBM CodePack : compress standard instruction set
  full 32-bit instruction in instruction cache
  compressed code kept in main memory, ROM, disk.
  Hash table (TLB)
Hitachi：special RISC instruction set for embedded applications.
  SuperH

## Slide 10: 2.11 The Role of Compilers
Understanding compiler technology is critical to designing an effective instruction set.
Assembly language programming has been largely replaced by compilers which work together with the hardware to optimize performance.
Therefore, design architectures to be compiler targets .
Notes: 编译器的目标（输出）是指令
系统结构 支持汇编程序设计（早期）
编译（现在）（代码质量、写编译程序的难易）

## Slide 11: Compilers and Architecture
What features of an architecture lead to high quality code ?
What "makes it easy" to write efficient compilers for an architecture ?

## Slide 12: The Structure of Recent Compilers

## Slide 13: About compiler
The goals of compiler
  All valid programs must be compiled correctly
  Fast speed of the compiled code
  fast compilation, debugging support, interoperability among languages
Multiple-pass structure’s advantage：
  Reduce compiler complexity
  Easy writing a bug-free compiler
Disadvantages：
  Phase-ordering problem
  e.g. global common subexpression elimination

## Slide 14: Optimizations Classification
High-level optimizations
  Procedure inlining
Local optimizations within a straight-line code fragment
  Common subexpression elimination、constant propagation、
Global optimizations extend the local optimizations across branches and introduce a set of transformations aimed at optimizing loops
Register allocation associates registers with operands
  Calculate expressions、transfer parameters、store variables
Processor-dependent optimizations attempt to take advantage of specific architectural knowledge

## Slide 15: The Impact of Compiler Technology on the Architect’s Decisions
Two important questions:
  How are variables allocated and addressed?
  How many registers are needed to allocate variables appropriately?
Three areas in which current high-level languages allocate the data：
  Stack：local variables; scalars(single variables)
  Global data area：global variables, constants; arrays
  Heap：dynamic objects; accessed with pointers
At least 16 GPRs + separate floating-point registers

## Slide 16: How the Architect Can Help the Compiler Writer ?
The difficulties of compiler
  Big program size
  Interactive
  complexity of compiler’s structure
Basic principle of the compiler
  Make the frequent case fast and the rare case correct

## Slide 17: Architect’s Guidelines
Provide regularity
Provide primitives, not solutions
  Providing special features that "match" language constructs is NOT a good idea.
  These features may be good only for a certain language.
  And, worse, they may match but do more or less than what's required.
Simplify trade-offs among alternatives
  If there are 20 ways to implement an instruction sequence, it makes it difficult for the compiler writer to choose which is the most efficient.
provide instructions that bind quantities known at compile time as constants.

## Slide 18: Summary for compiler’s role
At least 16 gerneral-purpose registers
all supported addressing modes apply to all instructions that transfer data
provide primitives instead of solutions
simplify trade-offs between alternatives
KEEP IT SIMPLE , Less is more
SIMD extensions are examples of good marketing than that of hardware-software codesign

## Slide 19: 2.12 The MIPS Architecture
MIPS emphasizes:
  A simple load-store instruction set
  Design for pipelining efficiency, including a fixed instruction set encoding
  Efficiency as a complier target
MIPS provides a good architectural model for study, because of:
  Popularity of this type of processor
  An easy architecture to understand

## Slide 20: Summary of the statistic data from above sections
B.2 Use GPRs with a load-store architecture
B.3 Addressing modes：
displacement(12-16), immediate(8-16), register indirect
B.4 Support the data size and types:
8-, 16-, 32-, and 64-bit integers and 64-bit IEEE 754 floating-point numbers
B.5 Support the simple instructions:
load, store, add, subtract, move register-register, and shift
B.6 compare equal, compare not equal, compare less, branch, jump, call, and return
B.7 Use fixed instruction encoding
B.8 Provide at least 16 GPRs, and all addressing modes apply to all data transfer instructions

## Slide 21: MIPS emphasizes
A simple load-store instruction set
Design for pipelining efficiency, fixed instruction set encoding
Efficiency as a compiler target

## Slide 22: MIPS Architecture
Registers for MIPS
  R0~R31, F0~F31, a few special registers
Data Types for MIPS
  8-bit bytes, 16-bit half words, 32-bit words, and 64-bit double words for integer data
  32-bit single precision and 64-bit double precision for floating point
Addressing Modes for MIPS Data Transfers
  Immediate, displacement
  ( register indirect ~ D=0
  absolute addressing ~ base register=R0)
  PC-relative addressing

## Slide 23: MIPS Register Conventions
Conventions
This is an agreed upon “contract” or
“protocol” that everybody follows
Specifies correct (and expected) usage,
and some naming conventions
Established part of architecture
Used by all compilers, programs,
and libraries
Assures compatibility

## Slide 24: MIPS Register Convention (cont.)
Important Ones for Now (shaded)
R0 Constant 0
R2 Return Value
R3 Can use as temporary
R4 First argument
R5 Second argument
R31 Return address

## Slide 25: MIPS Addressing Modes
addi R1, R0, 10
add R2, R0, R1

## Slide 26: MIPS Addressing Modes
lw R1, 100(R2)

## Slide 27: MIPS Addressing Modes
beq R1, R2, 100

## Slide 28: MIPS Addressing Modes
j 10000

## Slide 29: MIPS Operations(Fig.B.23, pB-37)

## Slide 30: Instruction layout of MIPS Fig.B.22, pB-35
I-type instruction
Encodes: loads and stores of bytes, half words, words, double words.
All immediate(rt  rs op immediate)
Conditional branch instructions(rs is register, rd unused)
Jump register, jump and link register
(rd = 0, rs = destination, immediate = 0)
6
opcode
rs
rt
immediate
6
opcode
rs
rt
rd
shamt
funct
opcode
Offset added to PC
5
5
16
R-type instruction
6
5
5
5
5
6
Register-register ALU operations: rd  rs funct rt
Function encodes the data path operation: Add, Sub, …
Read/write special registers and moves
J-type instruction
6
26
Jump and jump and link
Trap and return from exception
All instructions are encoded in one of three types, with common fields in the same
location in each format.

## Slide 31: Loading Immediate Values
What’s the largest immediate value that can be loaded into a register?
But, how do we load larger numbers?

## Slide 32: Load Upper Immediate

## Slide 33: Larger Constants?

## Slide 34: Procedure calls
Steps followed in executing a procedure call:
  Place parameters in a place where the procedure (callee) can access them
  Transfer control to the procedure
  Acquire the storage resources needed for the procedure
  Perform desired task
  Place results in a place where the calling program (caller) can access them
  Return control to the point of origin

## Slide 35: Resources Involved

## Slide 36: MIPS Register Convention

## Slide 37: Alternative Architectures
About MIPS as an ISA
  It’s a simple/small ISA;
  It emphasizes a small number of instructions, formats, address modes
Design alternative:
  Provide more powerful operations, and many of them
  Goal is to reduce number of instructions executed
  Danger is a slower cycle time and/or a higher CPI
Sometimes referred to as “RISC vs. CISC”
  RISC: Reduced Instruction Set Computing
  CISC: Complex Instruction Set Computing

## Slide 38: CISC vs. RISC
CISC (Complex Instruction Set Computer)
  Enhance the function of instructions, many kinds of operations, each instruction’s function is strong
RISC(Reduced Instruction Set Computer)
  Reduce the function of instructions, Provide basic instructions, each instruction’s function is weak
Two completely different directions for Instruction Set Architectures

## Slide 39: CISC
Complex Instruction Set Computer
  Background: lack of storage resource, emphasize compiler optimization
  Techniques: Enhance the function of the instructions, Design some complex instructions, instead of some functions which are originally implemented by software
CISC example was DEC VAX: min code size, make asm easy instructions from 1 to 54 bytes long!

## Slide 40: RISC
Reduce CPI:
CPUtime=Instr_Count * CPI * Clock_cycle
Reduce the instruction set:
only keep the most basic ones
Load/Store architecture
Simple instructions, simple addressing modes, fixed-length instruction format…

## Slide 41: A Brief history of RISC
Load/Store architecture：
CDC6600(1963)--CRAY1(1976)
IBM801(1979年),
first RISC computer
1980, Patterson(Berkeley) & Ditzel
first put forward RISC, RISC-,
1981, Hennessy(Stanford)
MIPS
Commercial RISC CPU after 1985:
MIPS1(1986) & SPARC V1(1987) …

## Slide 42: Some typical high performance RISC CPU
SUN, SPARC(1987)
MIPS, SGI:MIPS(1986)
HP, PA-RISC,
IBM, Motorola, PowerPC
DEC、Compaq, Alpha AXP
IBM RS6000(1990) first Superscalar RISC

## Slide 43: Summary of ISA
Architecture = what’s visible to the program about the machine
  Not everything in the deep implementation is “visible”
  The name for this invisible stuff is “the implementation”
A big piece of the ISA = assembly language structure
  Primitive instructions, execute sequentially, atomically
  Issues are formats, computations, addressing modes, encoding etc

## Slide 44: Summary of ISA
Two broad flavors:
  CISC: lots of complicated instructions
  RISC: a few, essential instructions
  Basically all recent machines are RISC, but the dominant machine of
  today, Intel x86, is still CISC (though they do RISC tricks in the guts…)
Example: MIPS

## Slide 45: History of ISA
60’ Stack----reduce the gap between high-level programming language and machine language.
70’ reduce the software cost, replacing software with hardware
80’ processor performance  simple ISA

## Slide 46: 90’s ISA
Address size doubles: 32bit 64bit
Optimization conditional branch via conditional execution
Optimization of cache performance via prefetch
Support of multimedia
Faster floating-point operations
Long instruction word
Increased Conditional Execution

## Slide 47: Homework

## Slide 48
THANK YOU
THANK YOU