## Slide 1: Computer Architecture ----A Quantitative Approach
陈文智
浙江大学计算机学院
chenwz@zju.edu.cn

## Slide 2: Three Questions
What is pipelining?
How is the pipelining implemented?
What makes pipelining hard to implement?

## Slide 3: Definition
Pipelining is an implementation technique whereby multiple instructions are overlapped in execution; it takes advantage of parallelism that exists among the actions needed to execute an instruction.
Today, pipelining is the key implementation technique used to make fast CPUs.
Not only for CPU: a 12 level pipeline for geometry transformation in GPU(Clark 1982)

## Slide 4: Parallelism
From dictionary: the quality or condition of being parallel; a parallel relationship.
The Nature of a TASK. Goal in parallel computing and Arch. design : seek parallelism and try using it to improve performance.

## Slide 5: What is Pipelining ?
Pipelining:
  “A technique designed into some computers to increase speed by starting the execution of one instruction before completing the previous one.”
  ----Modern English-Chinese Dictionary
  implementation technique whereby different instructions are overlapped in execution at the same time.
  implementation technique to make fast CPUs

## Slide 6: It likes Auto Assembly line
An arrangement of workers, machines, and equipment in which the product being assembled passes consecutively from operation to operation until completed.
Ford installs first moving assembly line in 1913. The right picture shows the moving assembly line at Ford Motor Company’s Michigan plant.
( 84 distinct steps)

## Slide 7: Trucking gas from depot to gas station
The steps:
  Get the barrels
  Load them into the truck
  Drive to the gas station
  Unload the gas
  Return for more oil
Let’s do the math
  Each truck can carry 5 barrels
  Can load a truck with 5 barrels in 1 hour
  It takes each truck 1 day to drive to and from gas station
  How many barrels per week are delivered?

## Slide 8: Looks a Lot Like a Multi-cycle Processor
What are the steps ?
  Fetch an instruction (Get the barrels)
  Decode the instruction (Load them into the truck)
  ALU OP (Drive to the gas station)
  Memory Access (Unload the gas)
  Write-back (Return for more oil)

## Slide 9: A better way, but dangerous
Roll the barrels down the road
  Big fire hazard

## Slide 10: Big idea: Build a pipeline
Now let’s do the math
  Pipeline can accept 1 barrel every hour
  How many barrels get delivered to the gas station per day?

## Slide 11: Trucking vs. Pipelines
Trucks
  Truck with 5 barrels takes 1 day to drive to and from gas station, while need 2 hours for loading and unloading
  LOTS of TIME when loading area,gas station, and pieces of the road are unused
Pipelines
  Pipeline can accept 1 barrel every hour
  Resources (loading area, gas station,pipelines) are always in use

## Slide 12: Why Pipelining: Its Natural
Laundry
  Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, and fold
  Washer takes 30 minutes
  Dryer takes 40 minutes
  “Folder” takes 20 minutes
A
B
C
D

## Slide 13: Sequential Laundry
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Time
T
a
s
k
O
r
d
e
r

## Slide 14: Pipelined Laundry----Start work ASAP
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 15: Why pipelining : overlapped
Latches, called pipeline registers’ break up computation into 5 stages
Deal 5 tasks at the same time.
Only deal one task each time.
This task takes
“ such a long time”

## Slide 16: Why pipelining: more faster
Can “launch” a new computation every 100ns in this structure
Can finish 107 computations per second
Can launch a new computation every 20ns in pipelined structure
Can finish 5×107 computations per second

## Slide 17: Why pipelining : conclusion
The key implementation technique used to Make fast CPU: decrease CPUtime.
Improving of Throughput ( rather than individual execution time)
Improving of efficiency for resources (functional unit)

## Slide 18: What is a pipeline ?
A pipeline is like an auto assemble line
A pipeline has many stages
Each stage carries out a different part of instruction or operation
The stages, which cooperates at a synchronized clock, are connected to form a pipe
An instruction or operation enters through one end and progresses through the stages and exit through the other end
Pipelining is an implementation technique that exploits parallelism among the instructions in a sequential instruction stream

## Slide 19: Ideal Performance for Pipelining
If the stages are perfectly balanced, The time per instruction on the pipelined processor equal to:
Time per instruction on unpipelined machine
Number of pipe stages
So, Ideal speedup equal to
Number of pipe stages.

## Slide 20: Why not just make a 50-stage pipeline ?
Some computations just won’t divide into any finer (shorter in time) logical implementation.
5 stages OK
50 stages NO. Sorry!

## Slide 21: Why not just make a 50-stage pipeline ?
Those latches are NOT free, they take up area, and there is a real delay to go THRU the latch itself.
  Machine cycle > latch latency + clock skew
In modern, deep pipeline (10-20 stages), this is a real effect
Typically see logic “depths” in one pipe stage of 10-20 “gates”.
At these speeds, and with this few levels of logic, latch delay is important

## Slide 22: How Many Pipeline Stages?
E.g., Intel
  Pentium III, Pentium 4: 20+ stages
  More than 20 instructions in flight
  High clock frequency (>1GHz)
  High IPC
Too many stages:
  Lots of complications
  Should take care of possible dependencies among in-flight instructions
  Control logic is huge

## Slide 23: Simple implementation of a RISC Instruction Set (MIPS)
Start with Implementation without pipelining
  single-cycle implementation
  multi-cycle implementation
Pipelining the RISC Instruction Set
Pipelining performance issues
How can we do it efficiently ?
Examples

## Slide 24: How MIPS instruction set is implemented without pipelining ?
Five phases
  IF: Instruction fetch cycle
    Send PC to memory and fetch the Instruction
    Update the PC to NPC by adding 4
  ID: Instruction decode/ register fetch cycle
    Decode the instruction
    read the registers
    If needed, sign-extend the offset field of the instruction.

## Slide 25: The other three phases
  EX: Execution/ effective address cycle
    Memory reference: calculate the address
    R-R/ R-I ALU: ALU operation on R-R or R-I
    Branch: Do the equality test, compute the possible target address and send it to NPC if the equality test is true.
  MEM: Memory access
    Load: send the effective address to the data memory and fetch the data
    Store: write the data from the ID phases using the effective address.
  WB: Write-back cycle
    Load or ALU: write the result into the register file.

## Slide 26: Single-cycle implementation
seldom used !

## Slide 27: Multi-cycle implementation

## Slide 28: About Multi-cycle implementation
The temporary storage locations were added to the datapath of the unpipelined machine to make it easy to pipeline.
Note that branch and store instructions take 4 clock cycles.
  Assuming branch frequency of 12% and a store frequency of 10%, CPI is 4.78.
This implementation is not optimal.

## Slide 29: How to improve the performance ?
For a possible branch, do the equality test and compute the possible branch target by adding the sign-extended offset to the incremented PC earlier in ID.
Completing ALU instructions during the MEM cycle
So, branch instructions take only 2 cycles, store and ALU instructions take 4 cycles, and load instruction takes the longest time 5 cycles.
CPI drops to 4.07 assuming 47% ALU operation frequency.
2×12％ ＋4×（10％＋47％）＋ 31%×5＝4.07

## Slide 30: Optimized Multi-cycle implementation
Temporary storage locations

## Slide 31: Improvement on hardware redundancy
ALU can be shared.
Data and instruction memory can be combined since access occurs on different clock cycles.

## Slide 32: Pipelining MIPS instruction set
Since there are five separate stages, we can have a pipeline in which one instruction is in each stage.
CPI is decreased to 1, since one instruction will be issued (or finished) each cycle.
During any cycle, one instruction is present in each stage.
Ideally, performance is increased five fold !

## Slide 33: 5-stage Version of MIPS Datapath
store
load
pipeline
registers or
latches

## Slide 34: How pipelining decrease the execution time?
If your starting point is
a single clock cycle per instruction machine then
  pipelining decreases cycle time.
a multiple clock cycle per instruction machine then
  pipelining decreases CPI.

## Slide 35: Single-cycle implementation vs. pipelining
Load
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Store
IF
ID
EX
MEM
WB
R-type
Single Cycle Implementation: CPI=1, long clock cycle
Clk
Load
Store
Waste
Cycle 1
Cycle 2
Pipeline Implementation: CPI=1, clock cycle  long clock cycle/5
Clk
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10

## Slide 36: Multi-cycle implementation vs. pipelining
Load
Store
R-type
Clk
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Clk
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Multip-Cycle Implementation: CPI=5,
Pipeline Implementation: CPI=1,
Load
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Store
IF
ID
EX
MEM
WB
R-type
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB

## Slide 37: How simple as this ! Really ?
store
load
pipeline
registers or
latches
Why need to add this line?

## Slide 38: Problems that pipelining introduces
Focus: different operations with the same data path resource on the same clock cycle is not possible. (structure hazard)
There is conflict about the memory !
Mem
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Ld/St
Instr 1
Instr 2
Instr 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Reg
Mem
Reg

## Slide 39: Separate instruction and data memories
Let’s split instruction and data cache
the memory system must deliver 5 times the bandwidth over the unpipelined version.
IM
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Ld/St
Instr 1
Instr 2
Instr 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
Reg
DM
Reg

## Slide 40: The conflict about the registers !

## Slide 41: Sometimes we can redesign the resource
allow WRITE-then-READ in one clock cycle (double pump)
  Two reads and one write required per clock.
  Need to provide two read port and one write port.
What happens when a read and a write occur to the same register ? ( Data hazard )

## Slide 42: Conflict occurs when PC update
Must increment and store the PC every clock cycle.
What happens when meet a branch ?
  Branches change the value of the PC -- but the condition is not evaluated until ID !
  If the branch is taken, the instructions fetched behind the branch are invalid !
This is clearly a serious problem ( Control hazard ) that needs to be addressed. We will deal it later.

## Slide 43: Must latches be engaged ? Yeah !
Ensure the instructions in different stages do not interfere with one another .
Through the latches, can the stages be combined one by one to form a pipeline.
The latches are the pipeline registers , which are much more than those in multi-cycle version
  IR: IF/ID.IR; ID/EX.IR; EX/DM.IR; DM/WB.IR
  B: ID/EX.B; EX/DM.B
  ALUoutput: EX/DM.ALUoutput, DM/WB.ALUoutput
Any value needed on a later stage must be placed in a register and copied from one register to the next, until it is no longer needed.

## Slide 44: performance issues in pipelining
Latency: The execution time of each instruction in pipelining does not decrease, instead, always longer than that of unpipelined machine.
Imbalance among stages reduces performance
Overhead rise from register delay and clock skew also contribute to the lower limit of machine cycle.
Pipeline hazards are the major hurdle of pipeline, which prevent the machine from reaching the ideal performance.
Time to “fill” pipeline and time to “drain” it reduces speedup

## Slide 45
THANK YOU
THANK YOU