## Slide 1: Computer Architecture ----A Quantitative Approach
陈文智
浙江大学计算机学院
chenwz@zju.edu.cn

## Slide 2: Lecture 3 for pipelining
The control hazard
How to solve the control hazard

## Slide 3: Pipelining Hazards
Taxonomy of Hazards
  Structural hazards
    These are conflicts over hardware resources.
    OK, maybe add extra hardware resources;
      or full pipelined the functional units(split duble bump);
      otherwise still have to stall
  Data hazards
    Instruction depends on result of prior computation which is not ready (computed or stored) yet
    OK, we did these, Double Bump, Forwarding path,
      software scheduling, otherwise have to stall
  Control hazards
    branch condition and the branch PC are not available in time to fetch an instruction on the next clock

## Slide 4: The Control hazard
Cause
  branch condition and the branch PC are not available in time to fetch an instruction on the next clock
  The next PC takes time to compute
  For conditional branches, the branch direction takes time to compute.
Control hazards can cause a greater greater performance loss for MIPS pipeline than do data hazards.

## Slide 5: Example: Branches
24
R0
R0

## Slide 6: Recall: Basic Pipelined Datapath

## Slide 7: Control hazard
24

## Slide 8: Dealing with the control hazard
Four simple solutions
  Freeze or flush the pipeline
  Predict-not-taken (Predict-untaken)
    Treat every branch as not taken
  Predict-taken
    Treat every branch as taken
  Delayed branch
Note:
  Fixed hardware
  Compile time scheme using knowledge of hardware scheme and of branch behavior

## Slide 9: Recall: solve the hazard by inserting stalls
48 or 72
24

## Slide 10: The pipeline status
Branch instruction | IF | ID | EX | MEM | WB |  | 
Branch Successor |  | IF | stall | stall | idle | idle | 
Branch successor+1 |  |  |  |  | IF | ID | EX
Branch successor+2 |  |  |  |  |  | IF | ID
Branch successor+3 |  |  |  |  |  |  | IF

## Slide 11: Flushing the pipeline
Simplest hardware:
  Holding or deleting any instruction after branch until the branch destination is know.
  Penalty is fixed.
  Can not be reduced by software.

## Slide 12: Stalls greatly hurt the performance
Problem:
  With a 30% branch frequency and an ideal CPI of 1, how much the performace is by inserting stalls ?
Answer:
  CPI = 1+30%３＝1.9
  this simple solution achieves only about half of the ideal performance.

## Slide 13: Always Stalling Hurts the Not- taken case

## Slide 14: How about assume Branch Not Taken

## Slide 15: Predict –not-taken
Hardware:
  Treat every branch as not taken (or as the formal instruction)
    When branch is not taken, the fetched instruction just continues to flow on. No stall
    If the branch is taken, then restart the fetch at the branch target, which cause 3 stall.(should turn the fetched instruction into a no-op)
Compiler:
  Can improve the performance by coding the most frequent case in the untaken path.

## Slide 16: What If Branch Was Taken…?
24

## Slide 17: How to do with the branch taken ?
24

## Slide 18: Alternative is assuming the branch always taken
Most branches(60%) are taken, so we should make the taken branch more faster. Why not try assuming the branch always taken?

## Slide 19: Predict –taken
Hardware
  Treat every branch as taken (evidence: more than 60% braches are taken)
  As soon as the branch target address is computed, assume the branch to be taken and begin fetching and executing at the target.
  Only useful when the target is known before the branch outcome.
  No advantage at all for MIPS 5-stage pipeline.
Compiler
  Can improve the performance by coding the most frequent case in the taken path.

## Slide 20: Pipeline status for predict-taken
Branch is taken: 1 stall
44 BEQ R1, 24 | IF | ID | EX | MEM | WB |  | 
48 AND R12, R2, R5 |  | IF | idle | idle | idle | idle | 
72 LW R4, 50(R7) |  |  | IF | ID | EX | MEM | WB
76 |  |  |  | IF | ID | EX | MEM
80 |  |  |  |  | IF | ID | EX
Branch is not taken: 3 stall
44 BEQ R1, 24 | IF | ID | EX | MEM | WB |  | 
48 AND R12, R2, R5 |  | IF | idle | idle | idle | idle | 
72 LW R4, 50(R7) |  |  | IF | ID | idle | idle | idle
76 |  |  |  | IF | idle | idle | idle
48 AND R12, R2, R5 |  |  |  |  | IF | ID | EX

## Slide 21: Common Side-Effect in Pipelines
Sometimes, you just have to guess what will execute
  Often, we can do it right, and this saves cycles
  But, occasionally, we are wrong
Consequences
  We mistakenly start executing the wrong instructions
  To repair this, must make sure that they DO NOT really execute
  In particular, must ensure they do not incorrectly corrupt machine state

## Slide 22: Move the Branch Computation Forward

## Slide 23: Move the Branch Computation more Forward
store
load

## Slide 24: Result: New & Improved MIPS Datapath
Need just 1 extra cycle after the BEQ branch to know right address
On MIPS, its called - the branch delay slot
48 or 72
24

## Slide 25: Flushing : need only to insert one stall to resolve control hazard
48 or 72
40 ADD R30,R30,R30 | IF | ID | EX | MEM | WB |  | 
44 BEQ R1, 24 |  | IF | ID | EX | MEM | WB | 
48 AND R12, R2, R5 |  |  | IF | idle | idle | idle | idle
48 or 72 |  |  |  | IF | ID | EX | MEM

## Slide 26: Why “waste” the fetched instruction ?
We have fetched the instruction 48, why we fetch the second time if the branch not taken at last ?
48 or 72

## Slide 27: The pipeline status for predict-not-taken
40 ADD R30,R30,R30 | IF | ID | EX | MEM | WB |  | 
44 BEQ R1, 24 |  | IF | ID | EX | MEM | WB | 
48 AND R12, R2, R5 |  |  | IF | ID | EX | MEM | WB
52 OR R13, R6, R2 |  |  |  | IF | ID | EX | MEM
Branch is not taken: No stall
Branch is taken: 1 stall
40 ADD R30,R30,R30 | IF | ID | EX | MEM | WB |  | 
44 BEQ R1, 24 |  | IF | ID | EX | MEM | WB | 
48 AND R12, R2, R5 |  |  | IF | idle | idle | idle | idle
72 LW R4, 50(R7) |  |  |  | IF | ID | EX | MEM
76 |  |  |  |  | IF | ID | EX

## Slide 28: Delayed branch
Good news
  Just 1 cycle to figure out what the right branch address is
  So, not 2 or 3 cycles of potential NOP or stall
Strange news
  OK, it’s always 1 cycle, and we always have to wait
  And on MIPS, this instruction always executes, no matter whether the branch taken or not taken. (hardware scheme)

## Slide 29: Branch delay slot
Hence the name: branch delay slot
  The instruction cycle after the branch is used for address calculation , 1 cycle delay necessary
  SO…we regard this as a free instruction cycle, and we just DO IT
Consequence
  You (or your compiler) will need to adjust your code to put some useful work in that “slot”, since just putting in a NOP is wasteful (compiler scheme)

## Slide 30: How to adjust the codes?

## Slide 31: Example: rewrite the code (a)

## Slide 32: Example: rewrite the code (b-1)
Loop: LW R2, 0(R1)
ADD R3, R2, R4
SW R3, 0(R1)
……
SUB R1, R1, #4
BNEZ R1, Loop
LW R2, 0(R1)
Loop: ADD R3, R2, R4
SW R3, 0(R1)
……
SUB R1,R1, #4
BNEZ R1, Loop
LW R2, 0(R1)

## Slide 33: Example: rewrite the code (b-2)
Loop: LW R2, 0(R1)
ADD R3, R2, R4
SW R3, 0(R1)
DIV …..
……
SUB R1, R1, #4
BNEZ R1, Loop
Loop: LW R2, 0(R1)
ADD R3, R2, R4
DIV …...
…...
SUB R1, R1, #4
BNEZ R1, Loop
SW R3, +4(R1)

## Slide 34: Schedualing strategy vs. performance improvement

## Slide 35: Constrains of the delayed branch
There are restrictions on the instructions that are scheduled into the delay slots
The compiler's ability to predict accurately whether or not a branch is taken determines how much useful work is actually done.
For scheduling scheme b and c,
  It must be O.K. to execute the SUB instruction if the prediction is wrong.
  Or the hardware must provide a way of cancelling the instruction.

## Slide 36: Cancelling function
Includes the direction that the branch is predicted to go.
If branch is predicted incorrectly , CPU turns the instruction in the branch delay slot into a no-op.
Can reduce the complexity for compiler to select useful instructions into delay slot.

## Slide 37: Delayed branch with cancelling (of case b)

## Slide 38: Efficiency of delayed branch

## Slide 39: About delayed branch
Delayed branch are adopted in most RISC processors.
In general, the length of branch delay is more than 1 . However, always just one slot is used due to the compiler complexity.

## Slide 40: Performance comparison for four schemes
MIPS R4000, deeper pipeline
  Takes at least three pipeline stages before the branch target address is known
  An additional cycle before the branch condition is evaluated.
  Assuming branch frequencies as followed
    Unconditional branch 4%
    Conditional branch, untaken 6%
    Conditional branch, taken 10%

## Slide 41: Pipeline status for various schemes
uncond. L1 L2 L3 L4 L5 L6 2 stall
L1 s L1(branch target)
Stall pipeline: L1 L2 L3 L4 L5 L6 3 stall
L1 s s L1(branch target/i+1)
Predict taken:
L1 L2 L3 L4 L5 L6
taken: L1 s L1 L2 L3 2 stall
untaken: L1 s L1 idle 3 stall
L1(i+1)
Predict untaken:
L1 L2 L3 L4 L5 L6
untaken: L1 L2 L3 L4 L5 0 stall
taken: L1 L2 L3 idle 3 stall
L1 L2 idle
L1 idle
L1(branch target)

## Slide 42: Resolution

## Slide 43: Pipeline hazards
Taxonomy of Hazards
  Structural hazards
    These are conflicts over hardware resources.
  Data hazards
    Instruction depends on result of prior computation which is not ready (computed or stored) yet
  Control hazards
    branch condition and the branch PC are not available in time to fetch an instruction on the next clock
    OK, we did these: calculate the destination address and condition ASAP., Flushing the pipeline, predict-not-taken, predict-taken, delayed branch ( with/without cancelling)

## Slide 44: Summary for control hazard
Control hazards can cause a greater performance loss than do data hazards.
In general, the deeper the pipeline, the worse the branch penalty in clock cycles.
A higher CPI processor can afford to have more expensive branches.
The efficiency of the three schemes greatly depends on the branch prediction.

## Slide 45: Branch prediction
There are many different schemes
static branch prediction
  Assume taken
    This is surprisingly effective since 85% of backward branches and 60% of forward branches are taken.
  Assume not taken
  Predict by using profile information from previous run
dynamic branch prediction by hardware
  1-bit Branch Prediction
  2-bit Branch Prediction
  N-bit Branch Prediction
  Table-based Branch Prediction

## Slide 46: Accuracy of prediction based on profile

## Slide 47
0/1
转移指令
低位地址
预测行为
0：不转移
1：转移
预测失败取反

## Slide 48
T
T
Predict Taken
Predict Not
Taken
Predict Taken
Predict Not
Taken
11
10
01
00
T
NT
T
NT
NT

## Slide 49
If (d==0)
d=1;
if (d==1){
…...
}
设Reg[R1] = d
BNEZ R1, L1 ; br b1, (d!=0)
DADDIU R1, R0, #1 ; d==0, so d=1
L1: DADDIU R3, R1, # -1 ;
BNEZ R3, L2 ; br b2, (d!=1)
……
L2:

## Slide 52: 四种组合的含义：
注意：
  这里体现了相关性
  虽然上一次Br指令，并非一定是本次br指令，但在简单的loop中是可能的，如简单loop中不含其它br指令。

## Slide 53: 用这种相关预测器来预测上述例子。初值为NT/NT. （第一次迭代预测错，其余均正确）
粗体字表示本次预测
预测出错 b1动作与b2预测值选用关系
预测正确 b2动作与b1预测值选用关系
新预测值

## Slide 54
THANK YOU
THANK YOU